## Slide 1: Module 6
Implementing Network Services

## Slide 2: Module Objectives
Compare and contrast transport protocols.
Use command line tools to scan network ports.
Explain the use of network addressing services.
Explain the use of name resolution services.
Configure and troubleshoot DHCP and DNS services.
Notes: Suggested Instructional Tips – Learning Objectives
The learning objectives align with the following Exam Objectives for Module 5:
1.4 Explain common networking ports, protocols, services, and traffic types.
1.7 Given a scenario, use appropriate IPv4 network addressing.
3.4 Given a scenario, implement IPv4 and IPv6 network services.
5.3 Given a scenario, troubleshoot common issues with network services.
5.5 Given a scenario, use the appropriate tool or protocol to solve networking issues.

## Slide 3: Lesson 6.1
Transport & Application Layer Protocols

## Slide 4: Transport Layer
7 Application
6 Presentation
5 Session
4 Transport
3 Network
2 Data Link
1 Physical
Multiplexed application data delivery
Basic connectivity, address, and forwarding
Notes: Suggested Instructional Tips – Transport Layer
Emphasize that transport layer headers don't describe how to forward a packet across a network. They instruct a host what to do with the data in a packet, and how to verify that it is complete.

## Slide 5: Common TCP and UDP Ports
Port Number | Transport Protocol | Service or Application | Description
20 | TCP | ftp-data | File Transfer Protocol—Data
21 | TCP | ftp | File Transfer Protocol—Control
22 | TCP | ssh/sftp | Secure Shell/FTP over SSH
23 | TCP | telnet | Telnet
25 | TCP | smtp | Simple Mail Transfer Protocol
53 | TCP/UDP | domain | Domain Name System
67 | UDP | bootps | BOOTP/DHCP Server
68 | UDP | bootpc | BOOTP/DHCP Client
69 | UDP | tftp | Trivial File Transfer Protocol
Notes: Suggested Instructional Tip
Students should memorize this content.

## Slide 6: Common TCP and UDP Ports
Port Number | Transport Protocol | Service or Application | Description
80 | TCP | http | HTTP
110 | TCP | pop | Post Office Protocol
123 | UDP | ntp/sntp | Network Time Protocol/Simple NTP
143 | TCP | imap | Internet Message Access Protocol
161 | UDP | snmp | Simple Network Management Protocol
162 | UDP | snmp-trap | Simple Network Management Protocol Trap
389 | TCP/UDP | ldap | Lightweight Directory Access Protocol
443 | TCP | https | HTTP-Secure (Secure Sockets Layer (SSL)/Transport Layer Security (TLS)
445 | TCP | smb | Server Message Block over TCP/IP
Notes: Suggested Instructional Tip
Students should memorize this content.

## Slide 7: Common TCP and UDP Ports
Port Number | Transport Protocol | Service or Application | Description
514 | UDP | syslog | Syslog
546 | UDP | dhcpv6-client | DHCPv6 Client
547 | TCP | dhcpv6-server | DHCPv6 Server
587 | TCP | smtps | SMTP-Secure
636 | TCP | ldaps | LDAP-Secure
993 | TCP | imaps | IMAP-Secure
995 | TCP | pop3s | POP3-Secure
1433 | TCP | sql-server | MS Structured Query Language (SQL) Server
1521 | TCP | sqlnet | Oracle SQL*Net
Notes: Suggested Instructional Tip
Students should memorize this content.

## Slide 8: Common TCP and UDP Ports
Port Number | Transport Protocol | Service or Application | Description
3306 | TCP | mysql | MySQL/MariaDB
3389 | TCP | rdp | Remote Desktop Protocol
5004 | UDP | rtp | Real-Time Protocol
5005 | UDP | rtcp | Real-Time Control Protocol
5060 | TCP/UDP | sip | Session Initiation Protocol
5061 | TCP/UDP | sips | SIP-Secure
Notes: Suggested Instructional Tip
Students should memorize this content.

## Slide 9: Transmission Control Protocol (TCP)
TCP helps computers send information to each other in a reliable way.
For reliability, TCP requires numerous header fields to maintain state information.
Source port
Destination port
Sequence number
Ack number
Data length
Flags
Window
Checksum
Urgent Pointer
Options
Notes: Suggested Instructional Tips – Transmission Control Protocol (TCP)
TCP works like a delivery system that makes sure messages are fully received and in the right order. If something goes wrong or a message doesn't get to where it needs to go, TCP figures it out and fixes it, making sure everything gets delivered correctly.
The use of sequencing, acknowledgments, and retransmissions means that TCP requires numerous header fields to maintain state information.

## Slide 10: TCP Handshake
Host A
Host B
SYN
SYN + ACK
Connection Established
ACK
Hey! Let’s chat. Here’s my number.
I can talk now. Here’s my number.
Great! I’m
ready now!
Notes: Suggested Instructional Tips – TCP Handshake
Here’s a simple explanation:
SYN: The initiating device (let’s call it the client) sends a SYN (synchronize) message to the server to start the conversation. It’s like the client saying, “Hey, I want to talk, and I’m starting our conversation with this sequence number.”
SYN-ACK: The server responds with a SYN-ACK (synchronize-acknowledge) message. This means the server is saying, “Okay, I got your message, and I’m ready to talk too. Here’s my own sequence number for you to acknowledge.”
ACK: Finally, the client sends back an ACK (acknowledge) message to confirm it received the server’s sequence number. This is like the client saying, “Great, I got your sequence number, and here’s the acknowledgment that I’m ready to start our session.”
Once these three steps are completed, both the client and server have agreed on how to communicate, and the actual data transfer can begin. It’s a bit like a formal greeting before starting a meaningful conversation.

## Slide 11: UDP Exchange
Host A
Host B
Data
Data
Here is some data for you. I hope you get it!
I have some data for you too. No reply needed.
Notes: Suggested Instructional Tips – TCP Handshake
Here’s a simple explanation:
SYN: The initiating device (let’s call it the client) sends a SYN (synchronize) message to the server to start the conversation. It’s like the client saying, “Hey, I want to talk, and I’m starting our conversation with this sequence number.”
SYN-ACK: The server responds with a SYN-ACK (synchronize-acknowledge) message. This means the server is saying, “Okay, I got your message, and I’m ready to talk too. Here’s my own sequence number for you to acknowledge.”
ACK: Finally, the client sends back an ACK (acknowledge) message to confirm it received the server’s sequence number. This is like the client saying, “Great, I got your sequence number, and here’s the acknowledgment that I’m ready to start our session.”
Once these three steps are completed, both the client and server have agreed on how to communicate, and the actual data transfer can begin. It’s a bit like a formal greeting before starting a meaningful conversation.

## Slide 12: User Datagram Protocol (UDP)
UDP helps computers send information to each other in a non-guaranteed way.
Source port
Destination port
Message length
Checksum
Notes: Suggested Instructional Tips – User Datagram Protocol (UDP)
TCP works like a delivery system that makes sure messages are fully received and in the right order. If something goes wrong or a message doesn't get to where it needs to go, TCP figures it out and fixes it, making sure everything gets delivered correctly.
The use of sequencing, acknowledgments, and retransmissions means that TCP requires numerous header fields to maintain state information.

## Slide 13: Activity: Run netstat
Open the command prompt or Terminal.
Run netstat command to view all active connections and their respective ports.
Use additional options like -a or -p and observe the output. Try -b if you have local administrator privileges.
Notes: Suggested Activity – Run netstat
Netstat is a command-line tool used to display information about network connections on a system.
Helps troubleshoot network connectivity issues
Provides insights into active network traffic
Identifies open ports and potential security risks

## Slide 14: Lesson 6.2
DHCP
Notes: Exam Objectives Covered
1.4 Explain common networking ports, protocols, services, and traffic types.
3.4 Given a scenario, implement IPv4 and IPv6 network services.

## Slide 15: DHCP Process
Client
Server
DHCP Discover
DHCP Offer
I’m new here. I need an IP address!
Here’s an IP address for you!
Great thanks! I’ll take it.
DHCP Request
DHCP Ack
Sounds good. It’s all yours!
Notes: Suggested Instructional Tips – TCP Handshake
Here’s a simple explanation:
SYN: The initiating device (let’s call it the client) sends a SYN (synchronize) message to the server to start the conversation. It’s like the client saying, “Hey, I want to talk, and I’m starting our conversation with this sequence number.”
SYN-ACK: The server responds with a SYN-ACK (synchronize-acknowledge) message. This means the server is saying, “Okay, I got your message, and I’m ready to talk too. Here’s my own sequence number for you to acknowledge.”
ACK: Finally, the client sends back an ACK (acknowledge) message to confirm it received the server’s sequence number. This is like the client saying, “Great, I got your sequence number, and here’s the acknowledgment that I’m ready to start our session.”
Once these three steps are completed, both the client and server have agreed on how to communicate, and the actual data transfer can begin. It’s a bit like a formal greeting before starting a meaningful conversation.

## Slide 16: DHCP Reservations and Exclusions
DHCP Reservations
Ensures a device always receives the same IP address
Tied to a device’s MAC address
Ideal for devices that need a consistent IP address
DHCP Exclusions
Prevents a range of IP addresses from being assigned
A range of IP addresses is set aside and not distributed
Ideal for addresses statically assigned to devices
Notes: Suggested Instructional Tips – DHCP Reservations and Exclusions
Configuring static assignments and/or reservations adds management overhead. But discuss reasons why it might be necessary such as logging/monitoring/authentication servers or printers that cannot be accessed by name.

## Slide 17: Activity: Identify the Protocol
1
3
2
Notes: Suggested Activity – Identify the Protocol
Answers:
TCP
UDP
DHCP

## Slide 18: Lesson 6.3
APIPA and SLAAC
Notes: Exam Objectives Covered
1.7 Given a scenario, use appropriate IPv4 network addressing.
3.4 Given a scenario, implement IPv4 and IPv6 network services.

## Slide 19: APIPA
Automatic Private IP Addressing
How APIPA Works on a Device
Uses ARP to ensure address is unique
Devices can self-assign an IP address when DHCP servers unavailable
Assigns itself an address between 169.254.0.1 and 169.254.254.255
Only for local network use
Notes: Suggested Instructional Tips – APIPA
Students need to learn these ranges.
These addresses are from one of the address ranges reserved for private addressing (169.254.0.0/16). The first and last subnets are supposed to be unused.

## Slide 20: IPv6 Autoconfiguration
IPv6 Autoconfiguration Description
Types
Stateful Address Autoconfiguration (DHCPv6)
Allows devices on an IPv6 network to configure their own IP addresses without DHCP
Stateless Address Autoconfiguration (SLAAC)
Notes: Suggested Instructional Tips – IPv6 Autoconfiguration
Description:
Autoconfiguration allows devices on an IPv6 network to configure their own IP addresses without the need for DHCP.​
Types:
Stateless Address Autoconfiguration (SLAAC)​
Stateful Address Autoconfiguration (DHCPv6)

## Slide 21: SLAAC
Advantages
Limitations
Does not provide DNS server addresses
Simplified network configuration
No need for a central server
Limited adoption in certain environments
Function
Link-local address configuration
EUI-64 interface identifier
Duplicate Address Detection (DAD)
Notes: Suggested Instructional Tips – SLAAC
SLAAC: IPv6’s self-configuring IP address mechanism.
How SLAAC Works: Automatic IP address generation using device’s MAC address.
    Link-local address configuration: Initial temporary IP for network communication.
    EUI-64 interface identifier: Unique IP creation from device’s hardware address.
    Duplicate Address Detection (DAD): Ensures IP uniqueness to prevent conflicts.
Advantages of SLAAC: Simplifies network setup with no central IP management needed.
Limitations of SLAAC: Lacks automatic DNS settings and is not universally adopted.

## Slide 22: DHCPv6
Function
Advantages
DHCPv6 request and response
Address assignment and management
Lease time and renewal
Centralized control
Extensive network configuration options
Limitations
Requires dedicates server setup
More complex than SLAAC
Notes: Suggested Instructional Tips – DHCPv6
DHCPv6: Managed IP distribution and configuration for IPv6 networks.
How DHCPv6 Works: Server-based IP lease and management protocol.
    DHCPv6 request and response: Communication process for IP allocation.
    Address assignment and management: Organized IP distribution by a central server.
    Lease time and renewal: Temporary IP assignment with expiration and renewal options.
Advantages of DHCPv6: Centralized control with extensive network configuration options.
Limitations of DHCPv6: Requires dedicated server setup and is more complex than SLAAC.
Suggested Analogy
Imagine a library with a self-service kiosk:
Library (Network): This represents the IPv6 network where devices need IP addresses to communicate.
Books (Data Packets): Data packets traveling across the network are like books being borrowed and returned in the library.
Librarian (DHCP Server): In an IPv4 network (without autoconfiguration), a DHCP server acts like a librarian, assigning IP addresses (like library cards) to devices requesting them.
Self-Service Kiosk (IPv6 Autoconfiguration): In an IPv6 network with autoconfiguration, devices can obtain IP addresses on their own, similar to using a self-service kiosk at the library.
The device generates a unique address based on its network interface card (MAC address) and network prefix (like a pre-programmed borrowing limit on the kiosk).
The device then verifies the address with other devices on the network (like checking for availability at the kiosk) to ensure it's not already in use.

## Slide 23: Activity: Think About It
The university’s IT department is deploying IPv6 across its diverse campus network.
With a mix of student devices, administrative workstations, and IoT-enabled classroom technology, the team needs an autoconfiguration protocol that can handle dynamic environments and provide ease of management.
Which protocol should they use?
Notes: Suggested Activity – Think About It
This activity can be individual, group, or classroom.
Considerations for Discussion:
Stateless Address Autoconfiguration (SLAAC) may seem ideal given the no-server-required and easy deployment making it a good fit for the plug-and-play nature of student devices.
Stateful Address Autoconfiguration (DHCPv6) may seem ideal given its centralized control and ability to deliver additional network settings, which could be beneficial for administrative and IoT devices that require consistent network configurations.

## Slide 24: Lesson 6.4
DHCP Relay and Troubleshooting
Notes: Exam Objectives Covered
3.4 Given a scenario, implement IPv4 and IPv6 network services.
5.3 Given a scenario, troubleshoot common issues with network services.

## Slide 25: DHCP Relay Agent
Acts as a network bridge
Receives a DHCP broadcast messages from clients and forwards them to DHCP server
Enables clients to obtain IP address from a remote DHCP server
Notes: Suggested Instructional Tips – DHCP Relay
Network Bridge: A DHCP relay acts as a bridge that forwards DHCP messages between clients and servers located on different subnets.
Broadcast handling: It receives DHCP broadcast messages from clients, encapsulates them into packets, and forwards them to the DHCP server
Subnet communication: Enables clients on a subnet without a DHCP server to communicate with a remote DHCP server to obtain IP configuration

## Slide 26: DHCP Relay
Network A
Network B
DHCP Discover
DHCP Request
DHCP Offer
DHCP Ack
Relay Agent
DHCP Client (Different Network)
DHCP Server
DHCP Clients (Same Network)
Notes: Suggested Instructional Tips – DHCP Relay
Image:
DHCP discover is sent to the DHCP server via the DHCP Relay Agent
The DHCP server replies with a DHCP offer by including an available IP address.
The client will broadcast a DHCP request to the server. Note: The client may receive multiple offers from several servers, so the client will broadcast a DHCP request to notify all DHCP servers the IP address that it selects.
The selected server replies with a DHCP Ack if the IP is still available.

## Slide 27: IP Helper
IP Helper
Functionality
Cisco network device feature
Forwards DHCP and other broadcast traffic across different subnets
Translates broadcasts to unicast to cross subnet boundaries
Sends DHCP requests from clients to a server in a different subnet
Notes: Suggested Instructional Tips – IP Helper
IP Helper Steps
  When a router receives a broadcast request (e.g., DHCP request) from a host on one subnet, the IP Helper Address steps in.
  It converts the broadcast request into unicast traffic and relays it to the DHCP server located in a different subnet.
  This enables DHCP clients residing on separate subnets to acquire IP addresses from a central DHCP server.
Difference between relay agent and IP helper:
  DHCP Relay Agent:
    Specifically designed to forward DHCP messages between clients and servers across different subnets.
    Follows protocols like RFC 1542 and RFC 2131 to handle DHCP messages1.
  IP Helper:
  A broader term that may include the functionality of a DHCP relay agent.
  Can forward various types of UDP broadcast traffic, not just DHCP requests1

## Slide 28: Activity: Troubleshooting DHCP
Client received address already in use
Client is unable to reach external networks
What steps would you take to troubleshoot the following DHCP issues?
Notes: Suggested Activity – Troubleshooting DHCP
Answer a a class, in groups, or individually: What steps would you take to troubleshoot the following DHCP issues?
Answers will vary, but here are a few options:
  Client is unable to reach external networks
      Incorrect default gateway configuration
      Incorrect subnet mask
      Incorrect DHCP server
  Client received address that was already in use:
      Use exclusion ranges
      Enable conflict detection
      Implement ARP checks

## Slide 29: Lesson 6.5
Domain Naming System
Notes: Exam Objectives Covered
1.4 Explain common networking ports, protocols, services, and traffic types.
3.4 Given a scenario, implement IPv4 and IPv6 network services.

## Slide 30: Think About It: DNS
What is DNS (Domain Name System)?
Notes: Suggested Activity – Think About It
Answer as a class, in groups, or individually.
Possible descriptions:
Internet Phonebook: DNS is often described as the phonebook of the Internet, translating human-friendly domain names into machine-friendly IP addresses.
Hierarchical System: It is a hierarchical and distributed naming system that associates various information with domain names assigned to entities across the Internet.
Operational Process: When you type a web address into your browser, DNS servers take that domain name and translate it into an IP address, allowing your browser to locate and load the requested webpage.

## Slide 31: Domain Name Service (DNS)
Host Names
Domain Names
Local identifiers
Human-friendly names
Global identifiers
Hierarchical structure
Assigned by administrator
Unique on the local network
Avoids duplications on the Internet
Registered with a registrar
Notes: Suggested Instructional Tips – Domain Name Service (DNS)
Hostnames (DNS)
  Local Identifiers: Hostnames are labels assigned to devices on a network, serving as local identifiers within a domain1.
  Human-Friendly Names: They provide a human-friendly way to remember a specific location on the Internet, such as www in www.example.com2.
Domain Names (DNS)
  Global Identifiers: Domain names are unique identifiers across the Internet that form part of a URL, like example.com3.
  Hierarchical Structure: They follow a hierarchical structure, with subdomains and top-level domains (TLDs), allowing for organized delegation of naming authority.
You might want to mention that DNS label naming rules are de facto standards. Recommendations were put forward in RFC 1912. RFC 2181 later clarified that these rules about allowable characters should not apply. That apart, using nonstandard punctuation in labels is an unnecessary risk.

## Slide 32: DNS Hierarchy
Root Domain
Top Level Domain
Domain
Sub-Domain
Root DNS Servers
.com DNS Servers
.org DNS Servers
.gov DNS Servers
Comptia.org DNS Servers
Nist.gov DNS Servers
Cisco.com DNS Servers
Microsoft.com Servers
Owasp.org DNS Servers
Cisa.gov DNS Servers
Help.comptia.org
Notes: Suggested Instructional Tips – DNS Hierarchy
Root Level: Represented by a period (.), serving as the top of the DNS hierarchy with 13 root servers (A to M).
Top-Level Domains (TLDs): Divided into generic (.com, .org, .net), sponsored (.gov, .edu), and country code (.uk, .ca, .de) TLDs, directly below the root.
Second Level Domains: These are under TLDs and include specific domain names chosen by individuals or organizations.
ICANN: The Internet Corporation for Assigned Names and Numbers (ICANN) oversees the operation of generic TLDs, while country codes are managed by appointed organizations.
Make sure students can relate elements of an FQDN as a detailed roadmap for locating a specific house on a street within a city and state.
FQDN as a Roadmap: Imagine the FQDN as a detailed roadmap for locating a specific house on a street within a city and state.
DNS Hierarchy as the Navigation System: The DNS hierarchy acts as the navigation system that interprets the FQDN and directs your request to the correct location.

## Slide 33: Name Resolution Using DNS
Notes: Suggested Instructional Tips – Name Resolution Using DNS
Use the diagram to explain the roles of the different types of DNS servers involved in this process.
Most queries between name servers are performed as iterative lookups.
A recursive lookup means that if the queried server is not authoritative, it does take on the task of querying other name servers until it finds the requested record or times out.
Image Description
The steps are as follows.
Client queries www dot 515 web dot net
Local name server is not authoritative is 515 web dot net and does not have a cached record. It is configured to perform recursive querying and so contacts a root server using a pre-configured list of IP addresses.
Root server is not authoritative for the record but returns the server for the .net TLD.
net TLD is not authoritative but returns the name server for 515 web dot net.
The 515 web dot net name server is authoritative for the domain and returns the requested www dot 515 web dot net host record.
The local server caches the record and responds to the client.
The client now has an IP address for www dot 515 web dot net, which it caches.
Image Caption
DNS name resolution process. (Images © 123RF.com.)

## Slide 34: Resource Records
DNS name servers maintain the DNS namespace in zones.
A DNS zone will contain numerous resource records.
A single zone namespace may host records for multiple domains.
Resource records help to resolve queries for names and services into IP addresses.
There are numerous types of resource records.
Notes: Suggested Instructional Tips – Resource Records
Note that a zone must be configured with both SOA and NS records. The SOA identifies the primary name server, plus contact and version information. There is only one SOA record. Other servers use NS records to identify the IP address of servers holding the domain's resource records. There can be multiple NS records, for redundancy.
DNS name servers maintain the DNS namespace in zones. - This sets the stage by explaining how the DNS information is organized.
A single zone namespace may host records for multiple domains. - This clarifies that a zone can manage multiple domain names within its scope.
A DNS zone will contain numerous resource records. - This details the specific type of information stored within a zone.
Resource records help to resolve queries for names and services into IP addresses. - This explains the purpose of resource records within a zone - translating names to IP addresses.

## Slide 35: Host Record Types
Start of Authority (SOA) | Host Address (A) for IPV4 Host Address (AAAA) for IPv6 | Mail Exchange (MX) | Service Records (SRV) | Text Records (TXT) | Pointer Records (PTR)
Indicate authority for a DNS zone Contain admin contact, refresh rates, and versioning information | Map domain names to IPv4 addresses Needed for DNS to translate domain names into IP addresses | Specify mail servers responsible for a domain Prioritize mail delivery | Identify service locations within a domain Include port numbers and priority for services | Store text information for external sources Used for SPF and DKIM records to reduce spam | Used for reverse DNS lookup Map IP addresses back to domain names

## Slide 36: DNS Server Configuration
Primary DNS Servers
Translate domain names into IP addresses
Act as the first point of contact for DNS queries
Secondary DNS Servers
Provide redundancy and load balancing for DNS queries
Serve as backup servers if the primary server fails
Cache-only DNS servers
Cache DNS resolutions to speed up response times
Handle repetitive queries to reduce load on primary/secondary servers
Notes: Suggested Instructional Notes – DNS Server Configuration
Primary DNS Servers
  Translate domain names into IP addresses
  Act as the first point of contact for DNS queries
Secondary DNS Servers
  Provide redundancy and load balancing for DNS queries
  Serve as backup servers if the primary server fails
Cache-only DNS servers
  Store recent domain name request resolutions to speed up response times
  Reduce the load on primary/secondary DNS servers by handling repeat requests

## Slide 37: Internal vs. External DNS
External DNS Servers:
Public access: Resolves Internet domain names for users External management: Managed by providers, not local network Public focus: Primarily handles public domain to IP resolution
Internal DNS Servers:
Private network: Resolves internal domain names Internal control: Managed by IT for local network Security focus: Enhances network security by isolating traffic
Notes: Suggested Instructional Tips – Internal vs. External DNS
External DNS Servers:
  Accessible by users on the Internet for website name resolution.
  Managed by hosting companies or domain registrars.
  Primarily focused on resolving public domain names to IP addresses.
Internal DNS Servers:
  Used within a private network for internal name resolution.
  Managed and maintained by an organization's IT department.
  Improves network security by isolating internal network traffic.

## Slide 38: DNS Security
Threat | Solution
DNS spoofing and poisoning | DNSSEC (DNS Security Extensions)
Eavesdropping and interception attacks | DNS over TLS (DoT)
Interception attacks and tampering | DNS over HTTPS (DoH)
DNS tunneling and advanced attacks | Advanced DNS Firewall
Notes: Suggested Instructional Tips – DNS Security
DNSSEC (DNS Security Extensions)
  Mitigates the risk of DNS spoofing and poisoning by ensuring that the responses to DNS queries are authentic and have not been tampered with.
DNS over TLS (DoT)
  Protects against eavesdropping and interception attacks by encrypting the DNS query and response, ensuring that the DNS transaction is secure and private.
DNS over HTTPS (DoH)
Like DoT, DoH also encrypts DNS traffic to protect against interception and tampering. It also disguises DNS traffic as regular HTTPS traffic, which can circumvent censorship and enhance privacy.
Advanced DNS Firewall
  Defends against DNS tunneling and other sophisticated DNS-based attacks by inspecting DNS traffic for anomalies, enforcing policies, and blocking malicious activities.

## Slide 39: Activity: Two Truths and a Lie
Host names help to avoid duplications on the Internet
Resource records help resolve queries for names and services into IP addresses
Pointer records map IP addresses back to domain names
Notes: Suggested Activity – Two Truths and a Lie
Answer: Host names help to avoid duplications on the Internet
LIE – Host names are unique only the local network. Domain names avoid duplications on the Internet
Resource records help resolve queries for names and services into IP addresses
Pointer records map IP addresses back to domain names

## Slide 40: Lesson 6.6
DNS Troubleshooting
Notes: Exam Objectives Covered
3.4 Given a scenario, implement IPv4 and IPv6 network services.
5.5 Given a scenario, use the appropriate tool or protocol to solve networking issues.

## Slide 41: Client DNS Issues
Symptoms of DNS Issues
Timeouts and errors
Partial DNS failures
No access to Internet sites or services
Delays in accessing websites
Notes: Suggested Instructional Tips – Client DNS Issues
Symptoms of DNS Issues:
Timeouts and errors across multiple Internet applications, making it seem like your entire Internet connection is down.
Partial DNS failures affecting only some websites, where you can access certain sites, but others appear to be down.
Page loading issues, such as image placeholders, empty spaces where content should be, or non-functional site features due to DNS not resolving domains for site resources.
Delays in accessing websites, email failures, and a general degradation of Internet-dependent services.

## Slide 42: Name Resolution Issues
Name Resolution Methods
Check local name caches
Check HOSTS
Verify DNS records using nslookup or dig
Notes: Suggested Instructional Tips – Name Resolution Issues
Symptoms of DNS Issues:
Timeouts and errors across multiple Internet applications, making it seem like your entire Internet connection is down.
Partial DNS failures affecting only some websites, where you can access certain sites, but others appear to be down.
Page loading issues, such as image placeholders, empty spaces where content should be, or non-functional site features due to DNS not resolving domains for site resources.
Delays in accessing websites, email failures, and a general degradation of Internet-dependent services.
Note the importance of establishing the scope of the issue when troubleshooting name resolution.

## Slide 43: Activity: Run nslookup and dig
Windows Machines
  Open command prompt or Terminal
  Type ns lookup comptia.org
Linux or Mac Machines
  Open Terminal
  Type dig comptia.org
Notes: Suggested Activity – Run nslookup and dig
Nslookup results: The output will display the domain’s DNS records, including IP addresses.
Dig results: the output will show detailed DNS information, including the domain’s A records, MX records, and more.
Have learners try other domains as well.

## Slide 44: Summary
Implementing Network Services
Notes: Suggested Instructional Tips
Ask learners to summarize their key takeaways from this module
Conclude by going over main points on the next slide

## Slide 45: Main Points
TCP (Transport): Reliable, connection-oriented, and error-checked data delivery (acknowledgments)
User Datagram Protocol (UDP): Works at the Transport layer; unlike TCP, it’s a connectionless, nonguaranteed method of communication with no acknowledgments or flow control
DHCP (Automatic IP): Assigns IP addresses, subnet masks, and optional parameters (gateway, DNS)
Relay Agents (DHCP): Forward DHCP traffic between subnets
DNS (Global Hierarchy): Translates domain names to IP addresses
Notes: Reiterate the relevance of each point:​
TCP works at the Transport layer to provide connection-oriented, guaranteed communication using acknowledgments to ensure that delivery has occurred.
DHCP provides an automatic method for allocating hosts an IP address, subnet mask, and optional parameters, such as the default gateway and DNS server addresses.
DHCP relay agents can be configured to provide forwarding of DHCP traffic between subnets.
DNS is a global hierarchy of distributed name server databases that contain information on domains and hosts within those domains.